## Slide 1: Advanced Hands On OpenCLTM
Simon McIntosh-Smith
James Price
Tom Deakin
Includes contributions from: Timothy G. Mattson (Intel), Benedict Gaster (UWE),
Dan Curran and Mike Boulton (University of Bristol)

## Slide 2: Course materials
Download the course slides, exercises and solutions:
http://www.cs.bris.ac.uk/~simonm/OpenCL/IWOCL_2016.zip

## Slide 3: Course materials
In addition to these slides, C++ API header files, exercises and solutions, it is useful to have:
OpenCL Reference Cards
These cards will help you keep track of the API as you do the exercises:
https://www.khronos.org/registry/cl/
The spec is also very readable and recommended to have on-hand

## Slide 4: Exercise dependencies
OS X (recent)
  libsdl2
  OpenCL driver is built in
Ubuntu 14.10+ / Linux
  We installed these packages through apt-get
    mesa-common-dev
    libsdl2-dev
    libgl1-mesa-glx
  Any OpenCL driver (e.g. NVIDIA, AMD or Intel)
Windows
  Windows 7 or newer
  Visual Studio 2010 or newer
  Any OpenCL driver (e.g. NVIDIA, AMD or Intel)

## Slide 5: Remote machine
Bristol Zoo: ssh user@hpc.cs.bris.ac.uk
Username (e.g): train01
Password: workshop
SSH into one of the nodes to run
  yawai: NVIDIA K40c, K20c
  rekt: S9150, AMD A10-7850K APU
  ohmai: NVIDIA GTX980, GTX580
  awyiss: AMD R9295X2, S10000
Load the Intel OpenCL SDK (for CPUs) with
module load sdks/intel-opencl/4.6.0.92

## Slide 6: A quick recap of OpenCL

## Slide 7: It’s a Heterogeneous world
OpenCL lets Programmers write a single portable program that uses ALL resources in the heterogeneous platform
A modern computing platform includes:
One or more CPUs
One of more GPUs
DSP processors
Accelerators
… others?
From integrated CPUs in smartphones, tablets and laptops through high-end desktops and servers with discrete GPUs
Notes: Die photo is Intel 5th gen Haswell quad core with GT3e IRIS graphics.
From http://www.anandtech.com/show/7744/intel-reveals-new-haswell-details-at-isscc-2014
Samsung® Exynos 5 is a Dual core ARM A15 1.7GHz, Mali T604 GPU

## Slide 8: Microprocessor trends
Individual processors have many (possibly heterogeneous) cores.
The Heterogeneous many-core challenge:
How are we to build a software ecosystem for the Heterogeneous many core platform?
Third party names are the property of their owners.
61 cores
16 wide SIMD
NVIDIA® Tesla® K40
10 cores
16 wide SIMD
AMD® Tahiti
Intel® Xeon Phi™ coprocessor
32 cores
16 wide SIMD
15 cores
192 wide SIMD

## Slide 9: Many-core performance potential
5.7X FLOP/s speedup
3.1X memory bandwidth
16 cores of Sandy Bridge at 3.1 GHz

## Slide 10: Unlocking this potential
Need efficient, expressive, parallel programming languages
Also need cross-platform standards
Ideally not just for HPC so that they have sufficient momentum for the long term
OpenCL is the only parallel programming language that meets all these many-core requirements today

## Slide 11: Industry Standards for Programming Heterogeneous Platforms
OpenCL – Open Computing Language
Open, royalty-free standard for portable, parallel programming of heterogeneous parallel computing CPUs, GPUs, and other processors
CPUs
Multiple cores driving performance increases
GPUs
Increasingly general purpose data-parallel computing
Graphics APIs and Shading Languages
Multi-processor programming – e.g. OpenMP
Emerging Intersection
Heterogeneous Computing

## Slide 12: OpenCL Working Group within Khronos
Diverse industry participation
  Processor vendors, system OEMs, middleware vendors, application developers.
OpenCL became an important standard upon release by virtue of the market coverage of the companies behind it.
Third party names are the property of their owners.

## Slide 13: OpenCL progress
New OpenCL C++ kernel language based on a subset of C++14
  Significantly enhanced programmer productivity and code performance
  OpenCL C still supported to preserve kernel code investment
Support for the new Khronos SPIR-V intermediate language in core
  SPIR-V now used by both OpenCL 2.1 and the new Vulkan graphics API
Runs on any OpenCL 2.0-capable hardware
  Only driver update required

## Slide 14: Important OpenCL concepts

## Slide 15: OpenCL Platform Model
One Host and one or more OpenCL Devices
  Each OpenCL Device is composed of one or more Compute Units
    Each Compute Unit is divided into one or more Processing Elements
Memory divided into host memory and device memory
Processing Element
OpenCL Device
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Host
Compute Unit

## Slide 16: An N-dimensional domain of work-items
Global Dimensions:
  1024x1024 (whole problem space)
Local Dimensions:
  128x128 (work-group, executes together)
Choose the dimensions that are “best” for your algorithm
1024
1024
Synchronization between work-items possible only within work-groups:
barriers and memory fences
Cannot synchronize between work-groups within a kernel

## Slide 17: OpenCL Memory model
Private Memory
  Per work-item
Local Memory
  Shared within a
  work-group
Global Memory /Constant Memory
  Visible to all
  work-groups
Host memory
  On the CPU
Memory management is explicit: You are responsible for moving data from
host → global → local and back

## Slide 18: The basic platform and runtime APIs in OpenCL (using C)
arg [0] value
arg [1] value
arg [2] value
arg [0] value
arg [1] value
arg [2] value
In Order
Queue
Out of Order
Queue
GPU
Context
__kernel void
dp_mul(global const float *a,
global const float *b,
global float *c)
{
int id = get_global_id(0);
c[id] = a[id] * b[id]; }
dp_mul
CPU program binary
dp_mul
GPU program binary
Programs
arg[0] value
arg[1] value
arg[2] value
Buffers
Images
In Order
Queue
Out of Order
Queue
Compute Device
GPU
CPU
dp_mul
Programs
Kernels
Memory Objects
Command Queues

## Slide 19: Host programs
The host program is the code that runs on the host to:
  Setup the environment for the OpenCL program
  Create and manage kernels
5 main steps in all host programs:
  Define the platform … platform = devices+context+queues
  Create and Build the program (dynamic library for kernels)
  Setup memory objects
  Define the kernel (attach arguments to kernel functions)
  Submit commands … transfer memory objects and execute kernels

## Slide 20: The C++ Interface
Khronos has defined a common C++ header file containing a high level interface to OpenCL, cl.hpp
This interface is dramatically easier to work with1
Key features:
  Uses common defaults for the platform and command-queue, saving the programmer from extra coding for the most common use cases
  Simplifies the basic API by bundling key parameters with the objects rather than requiring verbose and repetitive argument lists
  Ability to “call” a kernel from the host, like a regular function
  Error checking can be performed with C++ exceptions
1 especially for C++ programmers…

## Slide 21: C++ interface example
#define N 1024
int main(void) {
vector<float> h_a(N), h_b(N), h_c(N);
// initialize these host vectors…
Buffer d_a, d_b, d_c;
Context context(CL_DEVICE_TYPE_DEFAULT);
CommandQueue queue(context);
Program program(context,
loadprogram(“vadd.cl”), true);
// Create the kernel functor
make_kernel<Buffer, Buffer, Buffer>
vadd(program, “vadd”);
// Create buffers
// True indicates CL_MEM_READ_ONLY
// False indicates CL_MEM_READ_WRITE
d_a = Buffer(context, h_a.begin(), h_a.end(), true);
d_b = Buffer(context, h_b.begin(), h_b.end(), true);
d_c = Buffer(context, CL_MEM_WRITE_ONLY,
sizeof(float) * N);
// Enqueue the kernel
vadd(EnqueueArgs(queue, NDRange(N)),
d_a, d_b, d_c);
copy(queue, d_c, hc.begin(), hc.end());
}
Note: The default context and command queue are used when we don't specify one in the function calls. The code here also uses the default device, so these cases are the same.