## Slide 1: Advanced OpenCL Topics: Host-DEVICE Interactions
Part 1

## Slide 2: Platform discovery
A machine may have any number of OpenCL platforms
Each with their own devices
Some devices may even be aliases across platforms (CPU, usually)
How can you reliably pick your devices?

## Slide 3: Hard coding
Only good if you know what machine your code will always run on
Simplest to implement
Often this simple approach is good enough
// get platforms
std::vector<cl::Platform> platforms;
cl::Platform::get(&platforms);
// get devices from the first platform
std::vector<cl::Device> devices;
platforms[0].getDevices(
CL_DEVICE_TYPE_ALL, &devices);
// create context from first device
cl::Context context(devices[0]);

## Slide 4: Selection
Pass platform & device numbers in command line or via GUI (with sane defaults)
Much more flexible
Needs a little more code
cl::Context getContext(int plat_num, int dev_num)
{
// get platforms
std::vector<cl::Platform> platforms;
cl::Platform::get(&platforms);
// get devices from the first platform
std::vector<cl::Device> devices;
platforms[plat_num].getDevices(
CL_DEVICE_TYPE_ALL, &devices);
// create context from device
return cl::Context(devices[dev_num]);
// remember: check ids are in range
}

## Slide 5: Interactive Selection
Provide an interactive interface for selecting the device at runtime
Give each platform/device a unique number
Much cleaner
But requires quite a bit more code
# alternatively, in python, this
# triggers interactive device
# selection (no C required!)
pyopencl.create_some_context(True)

## Slide 6: Multiple Devices
Running across multiple devices can deliver better performance (if your problem scales well)
But have to manually partition problem / load balance
Remember, the cost of moving data to/from a device is much greater than normal memcpy's, so avoid where possible
There are a couple of options for using multiple devices within OpenCL

## Slide 7: Multiple Contexts
The simplest method – just create a separate context and command queue for each device
This is only useful if you don’t need to move data between devices – clEnqueueCopyBuffer can’t work with memory objects created in different contexts
  All memory will have to be copied via host
CANNOT synchronize with events between command queues within different contexts!

## Slide 8: Multiple Command Queues
A context can support more than one device, although only within the same platform
This allows memory copies between devices
However, there must be a separate command queue for each device in the context
CAN synchronize with events between command queues within the same context!

## Slide 9: Shared Memory Objects
Memory objects can be shared across multiple devices that share a context
The runtime will ensure that data is copied between the devices as needed
However, synchronization must be performed explicitly, by providing event dependencies when enqueuing commands
Some platforms might not concurrently execute kernels on multiple devices that use the same memory objects, even if they don’t access overlapping regions
  You might be able to circumvent this with sub-buffers
  Separate kernel objects may also need to be used

## Slide 10: OpenCL & MPI
Using MPI, it is possible to use multiple devices
Typically, each MPI process gets a single device
This allows any number of OpenCL devices
However, moving memory between them can be very expensive

## Slide 11: Halo Exchange
If you can split your problem up into regions, then the edges may need to be synchronized across devices
OpenCL allows for copying rectangular regions of a 3D buffer with clEnqueueReadBufferRect/WriteBufferRect
This is good approach to get something working; however, in practice this method is usually quite slow
A much better alternative is to write kernels that will pack/unpack buffer regions into contiguous chunks that can be read directly, although this is much more complicated

## Slide 12: Pinned Memory
In general, the fewer transfers you can do between host and device, the better
But some are unavoidable
It is possible to speed up these transfers, by using pinned memory (also called page-locked memory)
If supported, can enable much faster host <-> device communications

## Slide 13: Pinned Memory
A regular enqueueRead/enqueueWrite command might manage ~6GB/s
But PCI-E Gen 3.0 can sustain transfer rates of up to 16GB/s
So, where has our bandwidth gone?
The operating system
Why? Let's consider when memory is actually allocated…

## Slide 14: Malloc Recap
Both OS X and Linux will oversubscribe memory
The pointer we got back, when accessed, will trigger a page fault in the kernel.
The kernel will then allocate us some memory, and allow us to write to it.

## Slide 15: Malloc Recap
Consider a laptop which has 16GB of RAM.
What is the output of the code on the right if run on this laptop?
#include <stdlib.h>
#include <stdio.h>
int main(int argc, char **argv)
{
// 64 billion floats
size_t len = 64 * 1024*1024*1024;
// 256GB allocation
float *buffer = malloc(len*sizeof(float));
if (NULL == buffer)
{
fprintf(stderr, "malloc failed\n");
return 1;
}
printf("got ptr %p\n", buffer);
return 0;
}

## Slide 16
% gcc test.c -o test
% ./test
got ptr 0x7f84b0c03350

## Slide 17: Malloc Recap
A non-NULL pointer was returned
Both OS X and Linux will oversubscribe memory
When will this memory actually get allocated?
Checking the return value of malloc/calloc is useless – malloc never* returns NULL!
#include <stdlib.h>
#include <stdio.h>
int main(int argc, char **argv)
{
// 64 billion floats
size_t len = 64 * 1024*1024*1024;
// 256GB allocation
float *buffer = malloc(len*sizeof(float));
if (NULL == buffer)
{
fprintf(stderr, "malloc failed\n");
return 1;
}
printf("got ptr %p\n", buffer);
return 0;
}
* This might not be true for an embedded system

## Slide 18: Malloc Recap
This program does not actually allocate any memory
We call malloc, but we never use it!
#include <stdlib.h>
#include <stdio.h>
int main(int argc, char **argv)
{
size_t len = 16 * 1024*1024;
float *buffer = malloc(len*sizeof(float));
return 0;
}

## Slide 19: Malloc Recap
So what happens here?
The pointer we got back, when accessed, will trigger a page fault in the kernel.
The kernel will then allocate us some memory, and allow us to write to it.
But how much was allocated in this code? Only 4096 bytes (one page)
#include <stdlib.h>
#include <stdio.h>
int main(int argc, char **argv)
{
size_t len = 16 * 1024*1024;
float *buffer = malloc(len*sizeof(float));
buffer[0] = 10.0f;
return 0;
}

## Slide 20: Malloc Recap
4KB pages will be allocated at a time, and can also be swapped to disk dynamically
In fact, an allocation may not even be contiguous
So, enqueueRead/enqueueWrite must incur an additional host memory to host memory copy, wasting bandwidth and costing performance

## Slide 21
EnqueueWrite:
  Allocate contiguous portion of DRAM
  Copy host data into this contiguous memory
  Signal the DMA engines to start the transfer
EnqueueRead:
  Allocate contiguous portion of DRAM
  Signal DMA engine to start transfer
  Wait for interrupt to signal that the transfer has finished
  Copy transferred data from the contiguous memory into memory in the host code’s address space

## Slide 22
Pinned memory side-steps this issue by giving the host process direct access to the portions of host memory that the DMA engines read and write to.
This results in much less time spent waiting for transfers!
Disclaimer: Not all drivers support it, and it makes allocations much more expensive (so it would be slow to continually allocate and free pinned memory)

## Slide 23: Using Pinned Memory
OpenCL has no official support for allocating pinned memory
But some vendors (e.g. NVIDIA) do support pinned memory allocations
We create an additional OpenCL buffer, and supply the CL_MEM_ALLOC_HOST_PTR flag
We never use this buffer on the device, but instead use enqueueMapBuffer to retrieve the host pointer
We can now use this host pointer in place of regular malloc/new allocations, and as arguments to enqueueRead/Write calls (to different OpenCL buffers)
To release this host pointer, we call enqueueUnmapMemObject before destroying the OpenCL buffer
// create additional device buffer
cl::Buffer d_pinned(
context,
CL_MEM_ALLOC_HOST_PTR,
bufferSize);
// map buffer
float *h_ptr =
(float*)queue.enqueueMapBuffer(
d_pinned, // device buffer
CL_TRUE, // blocking map
CL_MAP_READ, // read data*
0, // offset of region
bufferSize // amount of data to be mapped
);
// use buffer
// unmap buffer
queue.enqueueUnmapMemObject(d_pinned, h_ptr);
*Can be CL_MAP_READ, CL_MAP_WRITE or CL_MAP_WRITE_INVALIDATE_REGION (OpenCL 1.2).

## Slide 24: Caveats
Allocating pinned memory is much more expensive (about 100x slower) than regular memory, so frequent allocations will be bad for performance.
However, frequent reads and writes will be much faster!
Not all platforms support pinned memory. But, the above method will still work, and should not be any slower

## Slide 25: Zero-copy transfers
Some OpenCL platforms provide devices that have (physically) unified memory with the host
  Mobile/integrated GPUs
  CPU devices
We can detect these devices by querying the CL_DEVICE_HOST_UNIFIED_MEMORY flag
On these devices, it is wasteful to copy data between the host and device
We can instead create our buffers in a way that both the host and device can directly access the same region of memory
Notes: OpenCL 2.0 shared virtual memory will improve on this

## Slide 26: Zero-copy transfers
The OpenCL specification doesn’t describe zero-copy transfers, but all the vendors that support this recommend the same approach
We supply the CL_MEM_ALLOC_HOST_PTR flag when creating our device buffer
When we want to access the memory from the host, we map the buffer
The buffer must be unmapped before we can use it on the device again
// create device buffer in host-accessible mem
cl::Buffer d_buffer(
context,
CL_MEM_READ_WRITE | CL_MEM_ALLOC_HOST_PTR,
bufferSize);
// map buffer into host address space
float *h_ptr =
(float*)queue.enqueueMapBuffer(
d_buffer, // device buffer
CL_TRUE, // blocking map
CL_MAP_WRITE, // read data*
0, // offset of region
bufferSize // amount of data to be mapped
);
// use buffer on the host
memset(h_ptr, 42, bufferSize);
// unmap buffer
queue.enqueueUnmapMemObject(d_buffer, h_ptr);
// use buffer on device

## Slide 27: Exercise: Fast host-device data transfers
Start with the HostDevTransfer example
Improve the performance of the host-to-device data transfers by using pinned memory or zero-copy
Experiment with different sized buffers
Experiment with different devices
An example solution will be provided